## Slide 1: Hydrological monitoring: Towards trustworthy Data
Janelcy Alferes, Shehabeldeen Abdelfatah, Pieter Colpaert
Trust Triggers #1
20-04-202, Ghent, Belgium

## Slide 2
About Us
Janelcy Alferes
R&D
Project Leader Monitoring technology & Digital water at VITO
IWA Group on Instrumentation, Control and Automation (ICA)
Shehabeldeen Abdelfatah
PhD student at UGent
Researcher at VITO
Specialize in Linked Data and Data Spaces
FWO, 2023-2027
Water Fit for Reuse digital Architecture
and Modelling Ecosystem

## Slide 3: Data in the Water sector

## Slide 4: Big challenges and drivers
Source: Water Research Foundation (WRF)
Challenges across the entire water cycle
Resource recovery
GHGs
Sustainable
Energy
Water demand & Climate change
Contaminants of concern (CECs)
Net Zero target

## Slide 5: Big challenges and drivers
Complex system, suboptimal operation
Silo operations
Scattered amount of information
Data disconnected
Holistic approach, broader ecosystem
Safe & trustworthy exchange of data
Data standardization & interoperability
Models (operation & optimization)

## Slide 6: Big challenges and drivers
Transformation at all levels of water management
Efficient, robust & sustainable systems
Technologies: monitoring, ICT, modelling, AI…
From data to Intelligence
Transformation of raw facts into actionable insights with DATA as foundation
Ensure quality directives
Better management
Circular water
Increase awareness

## Slide 7: Big challenges and drivers
Process
Insights
Wisdom
Decision making
DATA VALUE
Measurements
Knowledge
Information
Data
Bottom-up approach
Data as core element for application of data-driven solutions
Water reuse

## Slide 8: Big challenges and drivers
From raw information to produce actionable insights and actions
1
2
3
Data standardization
Optimization algorithms
Ontologies & models
Surface Water management
Tackling Salinization in industrial harbor context
Optimization water treatment plants

## Slide 9: Big challenges and drivers
How do we trust the data?
How can we be sure the data isn't leading us down the wrong path?
Does more data equal more trust?
What is required towards trustworthy data?
From raw information to produce actionable insights and actions

## Slide 10: Big challenges and drivers
Make data accessible, interoperable and actionable.
Ensure consistency, reliability, security, and usability of the data towards water reuse & circularity.
From raw information to structured and interoperable data
1
Data standardization

## Slide 11: From unstructured to structure data

## Slide 12: Data sources
How do we take advantage of all available data sources at the same time? (query, visualize, calculate, predict)
Can we utilize real-time data?
Multiple data sources (different organizations & even countries) describe a single body of water
Each source comes with its own unique format, structure, and semantics (even language!).

## Slide 13: The solution … Linked data
Unstructured Data
Transformations
Structured Data
Available for users/uses
Multiple data sources
How can linked data lead to more trust?
1
Uses URIs for subjects, objects, and relationships
2
Semantic
Context
Verifiable Provenance
Built on top of Ontologies. By linking a data point to a globally defined term, everyone agrees on the exact meaning
3
Corroboration through Interconnectivity
If Dataset A links to Dataset B, & Dataset C also links to Dataset B to confirm the same fact, the "weight" of that truth increases
Transparency
follows Open World Assumption (OWA). information it has might be incomplete and provides links to find the rest
Reduced Human Intervention
manual "ETL" (Extract, Transform, Load) replaced by Federated Queries (using SPARQL). Data is queried directly from the source in real-time.
4
5

## Slide 14: What if the data we have is not Linked Data?
How to transform traditional (discrete) data into linked data
  We build pipelines to transform traditional (discrete) data into linked data
  Pipelines work in an automated fashion.
  Human intervention is needed to adjust for schema design/changes
1
2
Publishing Linked Data

## Slide 15: What we did to improve upon traditional linked data
1
Fragmented tree
Linked Data Event Streams (LDES)
Data is published as an append-only stream of immutable "events“ appended to existing data
Built-in Versioning (History)
Published in fragmented feeds, which makes it cheaper to query
Efficient synchronization. A client can "subscribe" to the stream and know exactly where they left off, catching up on only the missing events.

## Slide 16: What we did to improve upon traditional linked data
RDF Time Series Snippets (RDFTSS)
Data is compressed by separating redundant metadata from sensory readings
Significant reduction in ingest/recall size/time
Native support for data analysis tools
2

## Slide 17: How to consume linked data
Develop a Linked Data consumption-centric system.
Data is offered in multiple forms (LDES, LDESTSS, and CSV)
Decision support is provided in the form of querying, visualization, and forecasting.

## Slide 18: Case Studies

## Slide 19: Dessel–Kwaadmechelen canal
We started by monitoring two attributes: stage and discharge.
High-resolution historic data from 2021 to present.
Data obtained through Hydrologisch InformatieCentrum (HIC).

## Slide 20: Dessel–Kwaadmechelen canal use case
Stage
Discharge
Examining a selected window in June 2025, we noticed spikes in water discharge. This may indicate a change in the water level, probably caused by precipitation.

## Slide 21: Dessel–Kwaadmechelen canal usecase
Stage
Discharge
Precipitation
Examining a selected window in June 2025, we noticed spikes in water discharge. This may indicate a change in the water level, probably caused by precipitation.
Examining precipitation data, we noticed that the spike happened during a dry spell, eliminating prior conclusion.
The conclusion, lock operations lead to the discharge spikes

## Slide 22: Gent-Terneuzen Canal
We monitor canal conductivity levels through four sensors.
High-resolution historic data from 2021 to present.
Data obtained through Vlaamse Milieumaatschappij and .

## Slide 23: Gent-Terneuzen Canal use case
There's a clear long-term seasonal pattern, conductivity peaks in summer/autumn and drops in winter, repeating annually. This is typical for canals — lower rainfall and higher evaporation concentrate salts.

## Slide 24: Gent-Terneuzen Canal use case
Examining precipitation data, we notice that it has no noticeable effect on the canal’s conductivity.

## Slide 25: Gent-Terneuzen Canal use case
The conductivity value is higher on average in 2025 onward, suggesting recent behavior is more variable and harder to match to historical patterns.
The first recording of a conductivity value measuring over 10000 µS/cm in the year 2025 was in August, same month the new third lock became operational. Link

## Slide 26: What we learned from the use cases
Having data ≠ Sufficient data
There is a need to have

## Slide 27: Flemish smart data space
Smart Mobility
Water Management (flood, drought)
Agri-food
Environmental Monitoring

## Slide 28: Take home message
“without data, there is no information; without information, we know nothing; and a system that embeds no knowledge can not be intelligent” (Therrien et al., 2020)
Data can accelerate a successful transition towards efficient, & sustainable water systems.
“Good” and “enough” data leads to trust in data-driven decision making
Data standardization is paving the way towards Trustable use and exchange of data, facilitating interoperability and data solutions

## Slide 29
Janelcy Alferes
(janelcy.alferescastano@vito.be)
Shehabeldeen Abdelfatah
(shehab.ayman@vito.be)
Thank you!